## Slide 1: PWM Drawer
Eng/ Abdullah Abdelgalel
Group : D54

## Slide 2: TABLE OF CONTENTS 01 03 02 04
Overview
Program
Program Architecture and Modules
Test Results

## Slide 3: OVERVIEW 01

## Slide 4: INTRODUCTION
Pulse Width Modulation (PWM) is a widely used technique in electronics and electrical engineering for controlling the power delivered to electronic devices. PWM provides a means to efficiently regulate the average power supplied to a load by varying the duty cycle of a pulsating signal. The PWM Drawer Application is a software tool designed to facilitate the generation and customization of PWM signals for a variety of applications.

## Slide 5: SOME APPLICATIONS
Motor Control:
Regulate the speed and torque of motors with precision, crucial for robotics and industrial automation.
LED Dimming:
Achieve dynamic lighting effects and energy efficiency in LED applications.
Power Supply Regulation:

## Slide 6: Program Architecture and Modules 02

## Slide 7: Layerd Architecture Application Layer Hardware Abstraction Layer (HAL) Microcontroller Abstraction Layer (MCAL) PWM Drawer
PWM_Drawer
GLCD
DIO PWM ICU

## Slide 8: Program 03

## Slide 9: PWM Drawer Program Initilization
Initialize PWM
Initialize ICU
Initialize GLCD
Measure Signal
Get Duty Cycle from ICU
Draw Signal

## Slide 10: PWM Drawer Program Clear Input capture Flag Set Triggering Edge : Rising Edge
Wait for Input Capture
(Start)
Clear Input capture Flag and Timer Counter Set Triggering Edge :
Falling Edge
Measure Signal
Wait for Input Capture
(High Count)
Clear Input capture Flag and Timer Counter Set Triggering Edge :
Rising Edge
Wait for Input Capture
(Low Count)

## Slide 11: PWM Drawer Program Display Pattern until max pixel width (128)
Display Rising Edge
Display Pattern for
High Time
Draw Signal Shape
Display High Line Pattern
Display Falling Edge
Display Pattern For
Low Time
Display Low Line Pattern

## Slide 12: Test Results 04

## Slide 13
Note : All Generated PWM waves are generated from Timer 0. The Discussed Test Cases are for Fast PWM waves generated from the Microcontroller Atmega32.

## Slide 14: Test Case 1
Prescaler : 8
Duty : 60%
Expected output Frequency : 7.8125 KHz
Output Frequency : 8.298 KHz

## Slide 15: Test Case 2
Prescaler : 64
Duty : 60%
Expected output Frequency : 0.9765 KHz
Output Frequency : 0.982 KHz

## Slide 16: THANKS!
Do you have any questions?
aabduljalil70@gmail.com
+20 1030148185